## Slide 1: Measuring TNSP Outputs for Economic Benchmarking
AER Economic Benchmarking Workshop #5
2 May 2013
Denis Lawrence and John Kain

## Slide 2: Main Issue
Data requirements
Are there any variables missing from table 1 in section 3.2 that should be there?
Are the definitions proposed appropriate for economic benchmarking?
Should any of the definitions be altered to ensure consistency across TNSPs?

## Slide 3: Other Issues
Calculating output weights
Appropriate reliability measures for economic benchmarking
Including reliability measures as outputs
Network capacity, peak demand and throughput
Which peak demand?

## Slide 4: Revised outputs short list
measured and smoothed non–coincident terminal maximum demands
system capacity (taking account of both transformer and line/cable capacity)
number of entry and exit points, possibly adjusted for voltage levels
throughput (total or by broad user type or by location)
number of unplanned outage events
loss of supply event frequency
aggregate unplanned outage duration, and
number of protection system failure events

## Slide 5: Output Specification #1
Quantity | Value | Price
System capacity (kVA*kms) Entry & exit points (No) Throughput (GWh) Loss of supply events (No) Unplanned outage events (No) | Revenue * Cost share Revenue * Cost share Revenue * Cost share –1 * Loss of supply events * Average customers affected * VCR per customer interruption –1 * Unplanned outage events * Average customers potentially affected * VCR per customer interruption | Value / kVA*kms Value / No Value / GWh –1 * Average customers affected * VCR per customer interruption –1 * Average customers potentially affected * VCR per customer interruption

## Slide 6: Output Specification #2
Quantity | Value | Price
Smoothed non–coincident peak demand (MVA) Entry & exit points (No) Throughput (GWh) Unplanned outage duration (customer mins) Unplanned outage events (No) | Revenue * Cost share Revenue * Cost share Revenue * Cost share –1 * Customer mins * VCR per customer minute –1 * Unplanned outage events * Average customers potentially affected * VCR per customer interruption | Value / MVA Value / No Value / GWh –1 * VCR per customer interruption –1 * Average customers potentially affected * VCR per customer interruption

## Slide 7: Output Specification #3
Quantity | Value | Price
Smoothed non–coincident peak demand (MVA) Throughput (GWh) Loss of supply events (No) Unplanned outage duration (customer mins) Proper operation of equipment (No) | Revenue * Cost share Revenue * Cost share –1 * Loss of supply events * Average customers affected * VCR per customer interruption –1 * Customer mins * VCR per customer minute –1 * No events * Valuation per event | Value / MVA Value / GWh –1 * Average customers affected * VCR per customer interruption –1 * VCR per customer minute –1 * Valuation per event

## Slide 8: Operating environment short list
Variable | Definition | Source
Weather factors |  | 
Extreme heat days | Number of extreme cooling degree–days (above, say, 25° C) | BoM
Extreme cold days | Number of extreme heating degree–days (below, say, 12° C) | BoM
Extreme wind days | Number of days with peak wind gusts over, say, 90 km/hour | BoM
Terrain factors |  | 
Bushfire risk | Number of days over 50 per cent of service area subject to severe or higher bushfire danger rating | BoM & FAs
Rural proportion | Percentage of route line length classified as short rural or long rural | RIN
Vegetation encroachment | Percentage of route line length requiring active vegetation management | DNSPs
Service area factors |  | 
Line length | Route length of lines | RIN
Variability of dispatch | Proportion of energy dispatch from non–thermal generators | TNSPs
Concentrated load distance | Greatest distance from node having at least, say, 30 per cent of generation capacity to node having at least, say, 30 per cent of load | TNSPs